## Slide 1
49th Intelligent Sensing Program
Sensing in Precision (Digital) Agriculture
Notes: https://cordis.europa.eu/project/rcn/206207/factsheet/en
http://vinescout.eu/web/
This project has received funding from the European Union´s Horizon 2020 Programme under grant agreement no 737669
http://vinescout.eu/web/the-challenge-lab-to-field

## Slide 2: The company
Established in 1989 by Flemming CHRISTENSEN
  Employee Owned and a ’Life-Style’ company
  12x people with 300+ years experince
    4x with accredited Xilinx FPGA training
  Always designed and built our own products
  BSI - ISO9001-2015 certified, since 2003
Techology Focus
  Acceleration & Vision,
  Sensor & Robotics
2

## Slide 3
Overview
Hardware features
Sensors compatibility
Industry compatibility
Open software and firmware
PYNQ (Python) support
EDGE AI support
Applications
Endorsement
Summary
What Next?
Overview of the VCS-1 SYSTEM
Notes: * VCS was started in www.tulipp.eu, as flexible development platform for Low-Power Image Processing. It was expanded to cover multiple sensors during the www.vinescout.eu project.
VCS is a lightweight (300grams) electronics platform for “Vison, Control and Sensors” with a focus on controlling robots capable of operating in resilient environments such the ones that can be found in vineyards, orchards and greenhouses.
The primary design focus is edge AI, using low-power accelerators to provide processing-power when required and total power consumption is below 10 watts for the processing unit.
The VCS is built on a PC/104 PCB (90mm x 96 mm) – an industry standard form-factor with additional “Sundance External Interface Card” [SEIC] to provide I/O.
The SEIC is a low-cost PCB that can be removed from the processing board with a cable; also, possible to design a simple 4-layer PCB with ‘custom’

## Slide 4
A Xilinx Zynq MPSoC is the ‘heart’ of VCS-1 and provide 64-bit processor scalability while combining real-time control with soft and hard engines for graphics, video, waveform, and FPGA acceleration, using a Trenz TE0820 “SoM”.
HARDWARE FEATURES
Multiprocessor system
ZU4EV
TEO820-ZU4EV
Notes: Sundance is a “Certified Xilinx Alliance Partner” – and has been using Xilinx FPGA since 1993 to do acceleration
The choice of a Xilinx SoC/FGPA (Zynq) as the ‘heart’ of the VCS will give provide the processing power and low latency I/O
The Zynq is fitted onto VCS, using a 40mm x 50mm “SoM” (System-on-Module) to enable upgrade (or downgraded, to reduce performance/cost) of the VCS over time. The I/O interfaces/features of VCS are industry standard and not likely to require updates, as not on the critical path for AI processing
Application Unit (Quad-core 64-bit ARM Cortex A53 CPU)
  Required for running a Linux based OS/ ROS compatible
GPU (ARM Mali 400)
  Required for accelerating graphics.
RTU (ARM Cortex R5)
  Required for managing real-time events.
Programmable (FPGA) Logic
  Required for performing hardware acceleration of AI algorithms used to for on-the-fly image processing/classification.
I/O - a large selection of input/output standards are implemented directly on the Programmable Logic to reduce the latency between the various cameras, sensors and servo-motors, controlled by ROS or Python programming suits.

## Slide 5: Hardware FEATURES
Connectivity:
FM191-R; FMC-LPC to:
  15x Digital I/Os [DB9]
  12x Analogue Inputs [DB9]
  8x Analogue Outputs [DB9]
  1x Expansion [SEIC]
FM191-U; SEIC to:
  4x USB3.0 [USB-c]
  28x GPIO [40-pin GPIO]
FM191-A1; 40-pin GPIO
  28x GPIO [DB9]
FM191
I/O interfaces
Notes: The versatility of VCS is the modular concept of the SoM processing element on a PC/104 baord, combined with a separate I/O Module
Has plenty of ADC, DAC, I/O and expansion with PC/104

## Slide 6: Hardware FEATURES
A custom enclosure was specially designed for accommodating the VCS-1 system, called PC104-Blade
Rugged Enclosure
Notes: The PC104-Blade is a stackable concept for PC/104 boards. It will remove the need for any fans and provide a rugged environment for building solutions for embedded applications

## Slide 7: sensors compatibility
The VCS-1 is compatible with a wide range of sensors, like:
Depth sensor. Interface USB3.0
Intel RealSense - D435
Tracking sensor. Interface USB3.0
Intel RealSense – T265
Notes: VCS has multiple USB3 interfaces for interface to different cameras and sensors
  Intel RealSense D435 - Depth camera
  Intel RealSense T265 – Tracking camera
  Stereo Labs Zed Camera - Depth camera
  FLIR AX-8 - Thermal camera
Also, has all ‘typical’ interface to allow VCS to be a like a PC with HMDI display, SATA and Ethernet.
The ADC can get data from external sensors, etc.
The DAC can control servo-motors, etc.

## Slide 8: industry compatibility
VCS-1 features:
Raspberry Pi version 3 model B and Arduino compatible
Compatible with most of the Arduino/Raspberry Pi sensors and actuators
USB3.0 & Ethernet ports for interfacing with a wide range of sensors
Notes: Can connector with Raspberry PI and Arduino shields and actuactors

## Slide 9: hardware debug tools
VCS hardware debugging is easy with industry standard JTAG directedly into the Zynq MPSoC
TULIPP’s LynSyn Power Monitor & Toolchain
  http://bit.ly/VCS_Lynsyn
  http://bit.ly/VCS_Tulipp_Toolchain
Xilinx JTAG Platform Hardware Cable
  http://bit.ly/VCS_JTAG_Cable
Xilinx JTAG SmartLynq Cable
  http://bit.ly/VCS_SmartLynq_Cable
Notes: Can connector with Raspberry PI and Arduino shields and actuactors
Software support:
  ROS Melodic - Robotic platform
  MQTT – Machine-to-Machine” connectivity
  OpenCV 4.0.1 - Computer Vision Library
  Intel Movidius - Neuromorphic chip
  Python 2.7 and 3.6 support - Scripting Programming Language
  Ubuntu 18.04 LTS - Operating System
  Xilinx SDSoC environment (HLS – ‘C’ to ‘VHDL’)
  TULIPP’s STHEM Toolchain (on GitHub) with Lynsyn Power Monitor Unit (PMU)
  Xilinx DPU for Convolutional Neural Network

## Slide 10: open source
Open Source and online documentation:
CERN’s Open Hardware Repository
  http://bit.ly/VCS_OHR
VCS Hardware
  http://bit.ly/VCS_Hardware
VCS Software
  http://bit.ly/VCS_Software
VCS Firmware
  http://bit.ly/VCS_FM191_firmware
Notes: Documentation (user and reference manuals, schematics, software specs and wiki)
Hardware firmware and instructions on how to build it from scratch
Software (C/C++ Windows/Linux SDKs and demos using Artificial Intelligence Algorithms in C/C++ and python)
All the VCS firmware and software is available in the following GitHub repository:
  https://github.com/SundanceMultiprocessorTechnology/VCS-1

## Slide 11: VCS-1 Development tools
VCS’s “Processing System” (PS) running within the ARM A53 CPUs, is supported by Linux:
http://bit.ly/VCS_Xilinx_Linux
https://ubuntu.com/
VCS has a version of Ubuntu 16.04 LTS and 18.04 LTS ported and for free download.
Xilinx also offers free option of an embedded Linux for Zynq, called PetaLinux:
http://bit.ly/VCS_Peta_Linux
The VCS’s “Programable Logic” (PL) – that is the ‘classic’ FPGA fabric - is supported by the free WebPACK & SD-SoC environment from Xilinx:
http://bit.ly/VCS_Vivado_Zynq
http://bit.ly/VCS_C_to_VHDL_SDSoC
Notes: Software support:
  ROS Melodic - Robotic platform
  MQTT – Machine-to-Machine” connectivity
  OpenCV 4.0.1 - Computer Vision Library
  Python 2.7 and 3.6 support - Scripting Programming Language
  Ubuntu 18.04 LTS - Operating System
  Xilinx SDSoC environment (HLS – ‘C’ to ‘VHDL’)
  TULIPP’s STHEM Toolchain (on GitHub) with Lynsyn Power Monitor Unit (PMU)
  Xilinx DPU for Convolutional Neural Network

## Slide 12: programming tools
MQTT compatible
  OASIS standard
  Machine-to-machine (M2M)/"Internet of Things" connectivity protocol.
OpenCV compatible
  Open source computer vision and machine learning software library.
ROS compatible
  The Robot Operating System (ROS) is a set of software libraries and tools that helps building robot applications.
  ROS2 ready
PYNQ compatible
  PYNQ is an open-source project from Xilinx that is utilizing Python & Jupyter to make it easy to design embedded systems with Zynq

## Slide 13
The Xilinx Edge-AI Platform provides comprehensive tools and models which utilize unique deep compression and hardware-accelerated Deep Learning technology.
The platform provides efficient, convenient and economical inference deployments for embedded-CPU-based FPGAs.
The Xilinx AI team consists of renowned researchers and experienced professionals known for their pioneering work in the field of deep learning.
Edge-AI
Xilinx Edge - AI
The VCS-1 is fully compatible with the Xilinx Edge-AI.

## Slide 14
Key Features
Provides a complete set of toolchains with compression, compilation, deployment and profiling.
Supports mainstream frameworks and the latest models capable of diverse deep learning tasks
Provides a lightweight standard C/C++ programming API (no RTL programming knowledge required)
Scalable board support from cost-optimized to performance-driven platforms
Supports system integration with both SDSoC and Vivado
DNNDK consists of:
DEep ComprEssioN Tool (DECENT)
Deep Neural Network Compiler (DNNC)
Neural Network Runtime (N2Cube)
Profiler
Edge-AI
Xilinx-DPU
DNNDK™
(Deep Neural Network Development Kit)

## Slide 15
Edge-AI
Xilinx Edge-AI
Frameworks
Xilinx Edge-AI Platform supports a number of industry-standard frameworks
TensorFlow is an open-source framework developed by Google.
CAFFE is an open-source framework developed at UC Berkley.
Darknet is an open-source framework developed by Joseph Redmon.
Keras is a high-level neural networks API, written in Python and capable of running on top of TensorFlow.

## Slide 16
Edge-AI
Models

## Slide 17
Applications
http://bit.ly/VCS1_SLAM
http://bit.ly/VCS_Edge-AI

## Slide 18
http://bit.ly/VCS1_NDVI
http://bit.ly/VCS1_NN
VCS-1 Applications

## Slide 19
VCS-1 Applications
http://bit.ly/VCS1_VineScout

## Slide 20
http://bit.ly/VineScout_VCS_Summit_XL
http://bit.ly/Tullip_Use_Case_UAV
VCS-1 Applications

## Slide 21: VCS-1 Endorsement
Notes: http://tulipp.eu/advisory-board-endorsements/

## Slide 22: VCS-1 Endorsement
http://semfire.ingeniarius.pt/
Notes: http://tulipp.eu/advisory-board-endorsements/

## Slide 23: Summary
The VCS-1 has the following characteristics:
High performance, using ‘state-of-the-art’ Xilinx Zynq MPSoC
Low power consumption (typical 10W)
Highly compatible with a wide range of commercially available sensors and actuators
Highly optimised for computer vision applications, embedded AI and Deep Learning
Fully reconfigurable and expandable using PC/104 form-factor (90mm x 96mm)
Compatible with the most common Linux distros (I.e. Ubuntu, Debian, RedHat, CentOS, etc.)
Software support for ROS and MQTT
Python and C/C++ support

## Slide 24: WHAT’s next ?
Research topics:
  Object detection, changes detection, visual-servoing
  Autonomous navigation, object grasping
  2D>3D Pose estimation, perception, AI in robotics
Sundance University Program (SUP)
  Access to hardware prototypes
  Advisory Board Members
  BSC/MSc/PhD Internships
R&D Project proposals
  H2020, Innovate-UK, EuroSTARS
  EPSRC/BBSRC/UKRI/SPRINT
  https://www.smartagrihubs.eu/portal/network
Want to know more about Sundance in R&D Projects ?
https://www.sundance.com/sundance-in-eu-projects-programs/

## Slide 25: WHAT’s next ?

## Slide 26: WHAT’s next ?

## Slide 27
Sundance Multiprocessor Technology, Ltd.
Pedro Machado Pedro.M@sundance.com
Flemming Christensen Flemming.C@sundance.com